## Slide 1: Interferometer fundamentals
Adam Avison

## Slide 2: Outline
Why use an interferometer?
Two element interferometer
uv-coverage
A bit on calibration
Imaging data and Cleaning

## Slide 3: Why use an interferometer? - What do astronomers want?
High resolution
Parkes 64m
Lovell 76m
Efflesburg 100m
High sensitivity
Notes: Astronomers want everything... BIG DISHES REQUIRED

## Slide 4: Resolution
Imagine we want Hubble resolution:
D=2.4m, λ=600nm -> θ=0.05arcsec
At radio wavelengths, say 4.5cm (6.7GHz):
D would need to be ~185km
Sensitivity
Basically, the bigger the better!
Effective area of your dish

## Slide 5: How do we get it?
Interferometry
ALMA, 54 12m dishes and 12 7m dishes spread over 14km

## Slide 6: Most peoples first impression of interferometry
Dishes
Dark Arts
Pretty pictures
... hopefully by the end of this hour we’ll have cleared up the bit in the middle

## Slide 7: The two element interferometer

## Slide 8
Correlator’s function
Do the maths
Receiver outputs
Correlator output
The two element interferometer
What are we trying to do?
- Recreate the sky brightness distribution of astrophysical sources.
Delay between wavefronts arriving at x then y:
Notes: So the cross correlation of the two antenna outputs is the product of the correlator.
Equivalent to the multiplication of the Fourier transform of X times y’s fourier complex conjugate
cross-correlation is a measure of similarity of two series as a function of the lag of one relative to the other.

## Slide 9: That’s all well and good but how does this
tell us anything about the sky brightness distribution?

## Slide 10
...
v1 and v2, the voltage outputs of x & y are directly related to:
The brightness distribution, I(s), of the astronomical object
as seen over solid angle dΩ
and A(s) the area of the dish we use to observe it.
Leading to ...
Notes: Delta nu is a bandwidth term becase recievers don’t observe at a single frequency

## Slide 11
Adding in a bit more reality...
The vector s is comprise of the addition of s0 and σ (so s=s0 +σ).
We set τgeo to zero with instrumental delays
Meaning all delays in the data are from the vector σ
We then define the Complex Visibility as:
which is rather nice as V is the Fourier transform of I.
Notes: Sorry to switch from trig to exponential forms here but it just makes sense to me.

## Slide 12: Relating the visibility equation to the correlator output gives
Known!*
* After proper calibration

## Slide 13: A coordinate system for interferometry
l
m
We define u and v, as E-W and
N-S positions w.r.t w axis which
is parallel to s0.
l and m as direction
cosines of s we can write the
visibility equation as:
Given l and m are small the small angle approx applies and V(u,v) becomes a
direct Fourier transform of I(x,y)
Notes: Direction cosine = angle between vector s and s0 to the uv plane.
Remember we have one of these PER BASELINE

## Slide 14: In its full gory glory the... Measurement Equation
Vij = What we measure
Iν = What we want
Qij = additive errors
S = maps I to polarisation
i,j = telescope pair
Mij = Multiplicative baselines errors
Bij = Bandpass reponse
Gij = Gerenalised electronic gain
Dij = polarisation leakage
Eij = Antenna voltage pattern
Pij = paralatic angle
Tij =Tropospheric effects
Green= vectors
Blue= Scalars
Red= Part of the Jones Matrix
Slide cribbed from A.M.S.Richards
Notes: As used by CASA

## Slide 15: What we measure
Correlator output
Visibility equation
Dirty image
Eq. 1
Eq. 2
Eq. 3
Notes: The greater the number of UV points the greater our knowledge of I

## Slide 16: uv-coverage

## Slide 17: Filling the uv-plane
uv-coverage of an interferometer set out in a logarithmic spiral pattern comprised of two, five, ten and fifty antennas (top to bottom) and observing for 10 s, 2, 4, and 6 h (left to right).
t = 10s 2h 4h 6h
Nant =
2
5
10
50

## Slide 18: ASIDE: Antenna spacing to u, v, w
Lx, Ly, Lz = antenna coordinate differences
H0 , δ0 = hour-angle and declination of the phase reference position
λ = central frequency of observation

## Slide 19
We want to fill the uv-plane because the uv-coverage is the FT of the
synthesised beam, B. The greater the uv-coverage the better behaved the sidelobes are.
6 dishes
(~15 mins)
42 dishes
(~15 mins)
Filling the uv-plane

## Slide 20: Filling the uv-plane
For each antenna pair at each integration interval we get one uv measurement.
To optimize uv-coverage, thus giving us a ‘nicer’ synthesized beam we would ideally have:
1) A large number of dishes, thus more antenna pairs (N(N-1))
2) Greater time on source, more uv-points from the antennas we have.
3) An array configuration with a larger number of unique antenna spacings.

## Slide 21: Visual example

## Slide 22: A bit about calibration...
Notes: Not going to go into detail because it is kind of telescope dependent.

## Slide 23: All interferometers have the following steps in common.
Apriori steps. Some selection of system specific steps which need taking into account before standard calibration. We’ll ignore these
Bandpass calibration
Flux calibration
Gain calibration / Amp & phase calibration
Notes: 1) E.g. for ALMA WVR, Tsys etc.

## Slide 24: Bandpass calibration
Antenna based calibration. So solutions are per antenna w.r.t reference antenna.
Each receiver will have a unique response to emission at a given 𝜈.
But we know our BP cal has a flat spectrum (or known spectral index).
Calibrator needn’t be close to target on sky.

## Slide 25: Flux scaling
The visibility amplitudes which come out of the correlator have an arbitrary scaling.
To convert these into physically meaningful values we observe a source of known flux to which we can “bootstrap” the amplitudes values to.
Calibrator needn’t be close to the source. (But should avoid being low in the sky).
ALMA data of Titan for a given dataset (some bad
data here!).
Y-axis scale in correlator output units

## Slide 26: Flux scaling
The visibility amplitudes which come out of the correlator have an arbitrary scaling.
To convert these into physically meaningful values we observe a source of known flux to which we can “bootstrap” the amplitudes values to.
Calibrator needn’t be close to the source. (But should avoid being low in the sky).
CASA model of Titan for a given dataset
(Notice the y-axis scale)

## Slide 27: Flux scaling
This is typically a two part process, where by you set your amplitude scales with one task (e.g. setJy in CASA) and then scale the fluxes of other sources with another (e.g. fluxscale in CASA).
Fully calibrated data for Titan

## Slide 28: Complex Gain (Phase and Amplitude)
Calibration step to mitigate temporal effects (i.e. the atmosphere) on the phase and amplitude of the target source visibilities.
Target a bright, nearby (few degrees) quasar and intersperse throughout observation of target.
Needs to be nearby to be experiencing the same atmospheric conditions
Notice y-axis is factor 10 smaller!

## Slide 29: Complex Gain (Phase and Amplitude)
Notice y-axis is factor 10 smaller!
Scans on Science Target
Calibration step to mitigate temporal effects (i.e. the atmosphere) on the phase and amplitude of the target source visibilities.
Target a bright, nearby (few degrees) quasar and intersperse throughout observation of target.
Needs to be nearby to be experiencing the same atmospheric conditions

## Slide 30: Imaging and cleaning

## Slide 31: What we measure (reminder)
Correlator output
Visibility equation
Dirty image
Eq. 1
Eq. 2
Eq. 3
Notes: The greater the number of UV points the greater our knowledge of I

## Slide 32: Sampling function
Let us call the sampling of the uv-plane (aka uv-coverage), S, the sampling function
Given this the synthesized beam, B, is B=FT(S ).
And for each uv-point we have an observed visibility, V(u,v), so we can define the sampled visibility function as:
This is a truncated version of Chapter 7 (Briggs, Schwab & Sramek) of “Synthesis Imaging in Radio Astronomy II”
So V s=SV and from earlier (eq. 3) I D= FT(V S ) = FT (SV ). From which it follows that I D is the measured sky brightness
convolved with the synthesis beam, B.

## Slide 33: Weighting
This is a truncated version of Chapter 7 (Briggs, Schwab & Sramek) of “Synthesis Imaging in Radio Astronomy II”
Given this we can introduce weighting functions to control the shape of the synthesised beam.
DON’T WORRY TOO MUCH ABOUT THIS NOW, IT IS A SUBTLETY YOU NEED TO THINK ABOUT WHEN ACTUALLY IMAGING...
Rk = Weights relating to data quality, i.e. down weight bad data. This is observation dependent and we have no post observation control over it (so ignore).
Tk = Tapering function. Apply a tapering function (i.e. Gaussian), to the uv-coverage to for example downweight the outer uv-points lowering resolution.
Dk = Density weighting, applies some weight based on the clustering of uv points on a grid... This is the most commonly used type of weighting.
And as per the previous slide we can define the weighted and sampled visibility function as V W=WV.
Notes: Where delta is assumed to be a dirac delta sampling.... Need to ensure tis remains true via observation set up. And k represents the kth visibility

## Slide 34: Imaging the data
We now have the sampled and weighted visibilities, V W.
In order to efficiently make an image of our target sky brightness distribution, I, we need to take the Fourier transform of this using Fast Fourier Transforms (FFTs).
This requires the V W data to be gridded on to a regular grid.
This is done by convolution with some suitable gridding function*. Leaving us ultimately with some weighted and gridded visibilities which can be FFT’d to give us our dirty image ID.
*Discussion of gridding algorithms is a little beyond the scope of this workshop, please check the references
at the start of this talk for more information.

## Slide 35: CLEAN-ing
We’ve seen that our dirty image ID is the sky brightness distribution convolved with the synthesised beam B.
To get a better representation of the sky brightness distribution we need to remove the artefacts introduced by B. To achieve this we use CLEAN*
*As far as I know CLEAN is not an acronym, but it is usually captialised. I don’t know why?!

## Slide 36: Simple CLEAN overview
The Högbom (1974) CLEANing algorithm is the simplest CLEAN algorithm and is very illustrative of how CLEAN works
in general.
In words the Högbom algorithm works as follows:
Find the magnitude and position of peak emission in the dirty image.
Subtract from the dirty image the dirty beam, B, scaled by some gain value (i.e. 0.1). Creating a ‘residual’ image.
Note the position and magnitude subtracted as a point in a model.
Repeat 1-3 until a user defined threshold is reached, either some noise limit (in the residual) or a given number of iterations.
Convolve the final model with an idealised beam. I.e. a beam based on the interferometer if it was a huge single dish.
Or in a 2D example on the next page

## Slide 37: Högbom 2D example
True sky of 5 point sources
Dirty Beam (DB)
Dirty Image + noise, (DI)
Iteration 1
Residual Image after subtracting DB from peak in DI
CLEAN components in Model Image
*

## Slide 38: Högbom 2D example
True sky of 5 point sources
Dirty Beam (DB)
Dirty Image + noise, (DI)
Iteration n
Residual Image after subtracting several DBs from located
peaks in DI
CLEAN components in Model Image
*

## Slide 39: Högbom 2D example
True sky of 5 point sources
Dirty Beam (DB)
Dirty Image + noise, (DI)
Iteration FINAL
Residual Image after subtracting enough DBs from located peaks in DI until threshold met.
CLEAN components in model Image after final CLEAN
loop
*

## Slide 40: Högbom 2D example
CLEAN components in model Image after final
CLEAN loop
Idealized beam
Final reconstructed image
*

## Slide 41: ... and in 3D
True sky of 5 point sources
Dirty Beam (DB)
*
Dirty Image + noise, (DI)
 Increasing CLEAN cycles 

## Slide 42: ... and in 3D
True sky of 5 point sources
Dirty Beam (DB)
*
Dirty Image + noise, (DI)

## Slide 43
And after all that you’ll have a nice image/data cube from which you can actually do some Science!

## Slide 44: Which software to use?
Which telescope are you using?
Use CASA
ALMA
JVLA
eMerlin
ATCA
EVN
Has your supervisor insisted you use AIPS?
Use Miriad
SMA
GMRT
Use (EVIL) Miriad
Old MERLIN
Old VLA
Maybe use AIPS, but first try to...
Have you reminded your supervisor the year is 201x not 197x-199x?
YES
YES
NO
NO

## Slide 45: Further Reading
The slides from this talk are based on the fundamentals of interferometry which are explained in detail across:
“Interferometry and Synthesis in Radio Astronomy” - Thompson, Moran & Swenson
“Synthesis Imaging in Radio Astronomy II” – NRAO
“An introduction to Radio Astronomy” – Burke and Graham-Smith (4th edition out soon Burke, Graham-Smith (& Wilkinson?))
“Tools of Radio Astronomy” – Wilson, Rohfls & Hüttemeister
“The CASA Cookbook” – Ott & Kern et al.

## Slide 46: ¡Cheers!
Credit - xkcd.com
¿Questions?